## Slide 1: Lab 1: Introduction to SDRs
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Describe a SDR vs. a traditional custom hardware device
Describe the roles of the SDR and host in TX and RX processing
Compare real-time and non-real time processing
Set up the ADALM-Pluto for non real-time processing in MATLAB
Set up different configurations (loopback, non-loopbacks, one or two hosts)
Transmit samples in a continuous loop
Capture and visualize a frame of samples

## Slide 3: Excellent Reference
Free instruction book on SDRs
  Analog website
MATLAB exercises
Based on ADALM-Pluto
But a little theoretical

## Slide 4: SDRs vs. Custom Hardware
Traditional custom communication hardware device
  Ex: iPhone, Android, base stations (mostly)
  Custom integrated circuits
  Highly optimized
  Power efficient, small form factor, high performance
  Limited programmability of communications functions
Software defined radio
  Implemented in programmable components (FPGA, DSPs, Host PC)
  Limited functionality / processing speed
  Large form factor
  Not (typically) for commercial use
  Easy to change / program
  Excellent for learning, simple

## Slide 5: ADALM-Pluto
Simple, low-cost SDR
Lightweight
Can run on USB power
Sufficiently capable for basic experiments
WiFi and cellular emulation
NYU students will be provided one Pluto each
  Work in pairs for most labs

## Slide 6: ADALM-Pluto Capabilities
From Analog devices webpage

## Slide 7: Getting Started
Purchase Pluto device
  NYU students enrolled in class will get one device each to borrow for class
Install drivers on PC (Windows, Linux, or IOS)
Install MATLAB
All instructions available at MATLAB ADALM-Pluto webpage

## Slide 8: Inside the Pluto
Pluto
  RF up-conversion & down-conversion
  Filtering
  ADCs and DACs
  Interfaces with host via complex baseband samples
Host
  Performs all baseband processing
  This class we use MATLAB

## Slide 9: The 9361 Integrated Circuit
Transmitter:
  Upconversion
  ADC, Filtering, Power amplifier (PA)
Receiver
  Low-noise amplifier (LNA)
  Down-conversion, DAC, Filtering

## Slide 10: Non-Real Time Processing
This class: non-real time experiments
  Simple and channel is realistic
  But one-way, limited duration
Transmitter (TX)
  Load circular buffer once
  TX repeatedly sends same samples over and over again
Receiver (RX)
  Capture one frame of samples
  Load IQ samples into computer
  Process offline
RX Buffer
TX Buffer

## Slide 11: Configurations
Loopback
  One Pluto, one host
  Pluto performs TX and RX
  Easy but fixed, uninteresting RF channels
  Good for initial debugging
One host, two Plutos
  Requires only one host
  Channel limited by cable length
Two hosts, one Pluto each
  Most flexibility in channels
  But require two hosts
TX
RX

## Slide 12: Lab Submissions
Loopback
  Use for debugging only
  Do not submit
One host, two Plutos
  Allowed for submission
Two hosts, one Pluto each
  Allowed for submission
Work in pairs
  At NYU, each student has one Pluto
TX
RX

## Slide 13: Lab 1: Capturing and Receiving Samples